## Slide 1: MVS-6520/6530/3000 メカニカルブロック
ICP Software Description
2012.11 PSG CCS Dept.1

## Slide 2
1. Software Package
The ICP has the following software packages.
1-1. UI Application Package
1-2. UI FPGA Package

## Slide 3
1-1. UI Application Package
Board | File Name | Detail
CA-86 | app.img | Application
 | linux.img | Operating System (Linux)
 | u-boot-nand.bin | Boot Loader

## Slide 4
1-2. UI FPGA Package
Boad | File Name | Detail
CA-86 | panel_if_top.clf | Panel I/F
KY | panel_dev_top.clf | Panel Controller
< Note >
The installation of the UI FPGA can be installed from the Menu. It takes 10 minutes for installation.
After starting the installation, wait without doing anything until the message of END appears.

## Slide 5
2. Software Construction
MVS-8000G/X System
MVS-6500/3000 System

## Slide 6
2. Software Construction
The panel button status can be scanned by the SCU software.
Even the menu (Linux OS) is shut down, the panel buttons can be operated.
MVS-8000G/X System
MVS-6500/3000 System
The panel button status is scanned by the UI software and then its scan data is transferred to the SCU software.
When the menu （Linux OS） is shut down, the panel button operation is not possible.

## Slide 7
2. Software Construction
The SCU software controls the switcher, therefore, the operations of panel buttons and the menu cannot be operated when the SCU software stops.