## Slide 1: MVS-6520/6530/3000 メカニカルブロック
MVS Trobleshooting
2012.11 PSG CCS D1 Dept

## Slide 2: Agenda
Board Status
  LED on each board
Log Acquisition
  CA-85 SWER
  CA-85 SCU
How to specify the faulty board and a component
  MIX-55 Board
  XPT-34 Board
  DVP-55 Board
  FC-114 Board
  MY-119 Board
How to use tools
  Upgrading for the demo unit

## Slide 3: Board Status
For the LED on each board, see the following training materials.
  4.2. Electric and Software Descriptions of Processor Behavor

## Slide 4: How to get a log
  How to get the logs of CA-85 SWER/SCU
    Preparation
      3-pin serial cable（RS-232C）
      SerialUSB converter cable (*1)
      (*1) Only required if you do not have a 9-pin serial port
      on the PC
      PC
      Terminal soft （teraterm etc.)

## Slide 5: How to get a log
    Procedure
      Insert the 3-pin serial cable into the following each connector of CA-85 board.
      Connect the 3-pin serial cable to the PC. （*1）（*1)Use the serialUSB converter cable, if you do not have a 9-pin serial port on the PC.
      Start the terminal software on the PC.
SCU
＜CA-85 board＞
SWR

## Slide 6: How to get a log
    Procedure
      Set up the serial port as follows:
      Get the log.
Item | Value
Baud Rate | 115200
Data Bit | 8 bit
Parity | none
Stop Bit | 1 bit
Flow Control | none

## Slide 7
How to specify the faulty board and a component: MIX-55 (PP 8keyers)
 |  | Board_Name: | MIX-55 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | DVP-55
 |  | SLOT_No: | MVS-6530：SLOT2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | SLOT3
 |  | IC_Name: | MIXER | IMPIF1 | IMPIF2 | IMPIF3 | IMPIF4 | CADEC | IMP1 | IMP2 | IMP3 | IMP4 | mDDR1 | mDDR2 | mDDR3 | mDDR4 | mDDR5 | mDDR6 | mDDR7 | mDDR8 | 
 |  | REF_No: | IC001 | IC002 | IC003 | IC004 | IC005 | IC006 | IC007 | IC008 | IC009 | IC010 | IC1800 | IC1801 | IC1900 | IC1901 | IC2000 | IC2001 | IC2100 | IC2101 | 
DSK* (* = 1,2,,,,8) | Key ON/OFF | ON | DSK* | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 | DSK1 | DSK2/4 | DSK2 | DSK5/7 | DSK5 | DSK6/8 | DSK6 | 
 | Key Type | Pattern key |  |  |  |  |  |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 |  | else |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 | Key Fill | BUS |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 |  | MATTE |  |  |  |  |  |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 | Key Source | AUTO SEL |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 |  | SPLIT |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 | Key Border | Normal |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | else |  |  |  |  |  |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 | Main Mask | ON |  |  |  |  |  |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 | Processed Key | DME Select | DSK* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | DSK*
 |  | Resizer |  |  |  |  |  |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 | DSK1 | DSK2/4 | DSK2 | DSK5/7 | DSK5 | DSK6/8 | DSK6 | 
 | Transition Type | Common Wipe | DSK* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | DME_LINK | DSK* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | DSK*
 | Key Trans | Local Wipe |  |  |  |  |  |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 
 | Auto Chromakey | Sample Mark | DSK* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | CCR | ON |  | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BKGD* (* = A,B) | Transition Type | DME_LINK | BKGD* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | BKGD*
 |  | else | BKGD* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | CCR | ON | BKGD* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UTIL* | Wipe Border | UTIL BUS | UTIL* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PP_*OUT (* = PGM,PVW,CLN,KPVW) | FTB | ON | PP_*OUT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Preset Color Mix | ON | PP_*OUT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Trans_PVW | ON | PP_*OUT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ALL | Video_Format | change | ALL | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | ALL | DSK1/3 | DSK2/4 | DSK5/7 | DSK6/8 | DSK1/3 |  | DSK2/4 |  | DSK5/7 |  | DSK6/8 |  | 

## Slide 8
How to specify the faulty board and a component: MIX-55 (PP 4keyers)
 |  | Board_Name: | MIX-55 |  |  |  |  |  |  |  |  |  | DVP-55
 |  | SLOT_No: | MVS-6530/6520/3000：SLOT2 |  |  |  |  |  |  |  |  |  | SLOT3
 |  | IC_Name: | MIXER | IMPIF1 | IMPIF2 | CADEC | IMP1 | IMP2 | mDDR1 | mDDR2 | mDDR3 | mDDR4 | 
 |  | REF_No: | IC001 | IC002 | IC003 | IC006 | IC007 | IC008 | IC1800 | IC1801 | IC1900 | IC1901 | 
DSK* (* = 1,2,,,,4) | Key ON/OFF | ON | DSK* | DSK1/3 | DSK2/4 |  | DSK1/3 | DSK2/4 | DSK1/3 | DSK1 | DSK2/4 | DSK2 | 
 | Key Type | Pattern key |  |  |  |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 |  | else |  | DSK1/3 | DSK2/4 |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 | Key Fill | BUS |  | DSK1/3 | DSK2/4 |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 |  | MATTE |  |  |  |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 | Key Source | AUTO SEL |  | DSK1/3 | DSK2/4 |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 |  | SPLIT |  | DSK1/3 | DSK2/4 |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 | Key Border | Normal |  | DSK1/3 | DSK2/4 |  |  |  |  |  |  |  | 
 |  | else |  |  |  |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 | Main Mask | ON |  |  |  |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 | Processed Key | DME Select | DSK* |  |  |  |  |  |  |  |  |  | DSK*
 |  | Resizer |  |  |  |  | DSK1/3 | DSK2/4 | DSK1/3 | DSK1 | DSK2/4 | DSK2 | 
 | Transition Type | Common Wipe | DSK* |  |  |  |  |  |  |  |  |  | 
 |  | DME_LINK(MVS-65**) | DSK* |  |  |  |  |  |  |  |  |  | DSK*
 |  | DME_LINK(MVS-3000) |  |  |  |  | DSK1 | DSK2 | DSK1 | DSK1 | DSK2 | DSK2 | 
 | Key Trans | Local Wipe |  |  |  |  | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 
 | Auto Chromakey | Sample Mark | DSK* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON |  | DSK1/3 | DSK2/4 |  |  |  |  |  |  |  | 
BKGD* (* = A,B) | Transition Type | DME_LINK | BKGD* |  |  |  |  |  |  |  |  |  | BKGD*
 |  | else | BKGD* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON | BKGD* |  |  |  |  |  |  |  |  |  | 
UTIL* | Wipe Border | UTIL BUS | UTIL* |  |  |  |  |  |  |  |  |  | 
PP_*OUT (* = PGM,PVW,CLN,KPVW) | FTB | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Preset Color Mix | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Trans_PVW | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
ALL | Video_Format | change | ALL | DSK1/3 | DSK2/4 | ALL | DSK1/3 | DSK2/4 | DSK1/3 |  | DSK2/4 |  | 

## Slide 9
How to specify the faulty board and a component: MIX-55(ME1 4keyers)
 |  | Board_Name: | MIX-55 |  |  |  |  |  |  |  |  |  | DVP-55
 |  | SLOT_No: | MVS-6530：SLOT1、MVS-6520/3000：SLOT2 |  |  |  |  |  |  |  |  |  | SLOT3
 |  | IC_Name: | MIXER | IMPIF1 | IMPIF2 | CADEC | IMP1 | IMP2 | mDDR1 | mDDR2 | mDDR3 | mDDR4 | 
 |  | REF_No: | IC001 | IC002 | IC003 | IC006 | IC007 | IC008 | IC1800 | IC1801 | IC1900 | IC1901 | 
KEY* (* = 1,2,,,,4) | Key ON/OFF | ON | KEY* | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 | KEY3 | KEY2/4 | KEY4 | 
 | Key Type | Pattern key |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | else |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Fill | BUS |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | MATTE |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Source | AUTO SEL |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | SPLIT |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Border | Normal |  | KEY1/3 | KEY2/4 |  |  |  |  |  |  |  | 
 |  | else |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Main Mask | ON |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Processed Key | DME Select | KEY* |  |  |  |  |  |  |  |  |  | KEY*
 |  | Resizer |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Transition Type | Common Wipe | KEY* |  |  |  |  |  |  |  |  |  | 
 |  | DME_LINK(MVS-65**) | KEY* |  |  |  |  |  |  |  |  |  | KEY*
 |  | DME_LINK(MVS-3000) |  |  |  |  | KEY1 | KEY2 | KEY1 | KEY2 | KEY1 | KEY2 | 
 | Key Trans | Local Wipe |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Auto Chromakey | Sample Mark | KEY* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON |  | KEY1/3 | KEY2/4 |  |  |  |  |  |  |  | 
BKGD* (* = A,B) | Transition Type | DME_LINK | BKGD* |  |  |  |  |  |  |  |  |  | BKGD*
 |  | else | BKGD* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON | BKGD* |  |  |  |  |  |  |  |  |  | 
UTIL* | Wipe Border | UTIL BUS | UTIL* |  |  |  |  |  |  |  |  |  | 
PP_*OUT (* = PGM,PVW,CLN,KPVW) | FTB | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Preset Color Mix | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Trans_PVW | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
ALL | Video_Format | change | ALL | KEY1/3 | KEY2/4 | ALL | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 

## Slide 10
How to specify the faulty board and a component: MIX-55(ME2 4keyers)
 |  | Board_Name: | MIX-55 |  |  |  |  |  |  |  |  |  | DVP-55
 |  | SLOT_No: | MVS-6530：SLOT1 |  |  |  |  |  |  |  |  |  | SLOT3
 |  | IC_Name: | MIXER | IMPIF3 | IMPIF4 | CADEC | IMP3 | IMP4 | mDDR5 | mDDR6 | mDDR7 | mDDR8 | 
 |  | REF_No: | IC001 | IC004 | IC005 | IC006 | IC009 | IC010 | IC2000 | IC2001 | IC2100 | IC2101 | 
KEY* (* = 1,2,,,,4) | Key ON/OFF | ON | KEY* | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 | KEY3 | KEY2/4 | KEY4 | 
 | Key Type | Pattern key |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | else |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Fill | BUS |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | MATTE |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Source | AUTO SEL |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | SPLIT |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Border | Normal |  | KEY1/3 | KEY2/4 |  |  |  |  |  |  |  | 
 |  | else |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Main Mask | ON |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Processed Key | DME Select | KEY* |  |  |  |  |  |  |  |  |  | KEY*
 |  | Resizer |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Transition Type | Common Wipe | KEY* |  |  |  |  |  |  |  |  |  | 
 |  | DME_LINK(MVS-65**) | KEY* |  |  |  |  |  |  |  |  |  | KEY*
 | Key Trans | Local Wipe |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Auto Chromakey | Sample Mark | KEY* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON |  | KEY1/3 | KEY2/4 |  |  |  |  |  |  |  | 
BKGD* (* = A,B) | Transition Type | DME_LINK | BKGD* |  |  |  |  |  |  |  |  |  | BKGD*
 |  | else | BKGD* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON | BKGD* |  |  |  |  |  |  |  |  |  | 
UTIL* | Wipe Border | UTIL BUS | UTIL* |  |  |  |  |  |  |  |  |  | 
PP_*OUT (* = PGM,PVW,CLN,KPVW) | FTB | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Preset Color Mix | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Trans_PVW | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
ALL | Video_Format | change | ALL | KEY1/3 | KEY2/4 | ALL | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 

## Slide 11
How to specify the faulty board and a component : MIX-55 (ME3 4keyers)
 |  | Board_Name: | MIX-55 |  |  |  |  |  |  |  |  |  | DVP-55
 |  | SLOT_No: | MVS-6530：SLOT2 |  |  |  |  |  |  |  |  |  | SLOT3
 |  | IC_Name: | MIXER | IMPIF3 | IMPIF4 | CADEC | IMP3 | IMP4 | mDDR5 | mDDR6 | mDDR7 | mDDR8 | 
 |  | REF_No: | IC001 | IC004 | IC005 | IC006 | IC009 | IC010 | IC2000 | IC2001 | IC2100 | IC2101 | 
KEY* (* = 1,2,,,,4) | Key ON/OFF | ON | KEY* | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 | KEY3 | KEY2/4 | KEY4 | 
 | Key Type | Pattern key |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | else |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Fill | BUS |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | MATTE |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Source | AUTO SEL |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 |  | SPLIT |  | KEY1/3 | KEY2/4 |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Key Border | Normal |  | KEY1/3 | KEY2/4 |  |  |  |  |  |  |  | 
 |  | else |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Main Mask | ON |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Processed Key | DME Select | KEY* |  |  |  |  |  |  |  |  |  | KEY*
 |  | Resizer |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Transition Type | Common Wipe | KEY* |  |  |  |  |  |  |  |  |  | 
 |  | DME_LINK(MVS-65**) | KEY* |  |  |  |  |  |  |  |  |  | KEY*
 | Key Trans | Local Wipe |  |  |  |  | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 
 | Auto Chromakey | Sample Mark | KEY* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON |  | KEY1/3 | KEY2/4 |  |  |  |  |  |  |  | 
BKGD* (* = A,B) | Transition Type | DME_LINK | BKGD* |  |  |  |  |  |  |  |  |  | BKGD*
 |  | else | BKGD* |  |  |  |  |  |  |  |  |  | 
 | CCR | ON | BKGD* |  |  |  |  |  |  |  |  |  | 
UTIL* | Wipe Border | UTIL BUS | UTIL* |  |  |  |  |  |  |  |  |  | 
PP_*OUT (* = PGM,PVW,CLN,KPVW) | FTB | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Preset Color Mix | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
 | Trans_PVW | ON | PP_*OUT |  |  |  |  |  |  |  |  |  | 
ALL | Video_Format | change | ALL | KEY1/3 | KEY2/4 | ALL | KEY1/3 | KEY2/4 | KEY1/3 |  | KEY2/4 |  | 

## Slide 12
How to specify the faulty board and a component : XPT-34
山根さん
 |  | Board_Name: | XPT-34 (for MVS-6530/MVS-6520) |  |  |  |  | 
 |  | SLOT_No: | SLOT5 |  |  |  |  | 
 |  | IC_Name: | OUT | OUT | MV | DDR2 | MV | DDR2
 |  | REF_No: | IC003 | IC004 | IC005 | IC1701 | IC006 | IC1703
Output Process | Output | Video Clip | CH1-12 | CH13-24 |  |  |  | 
 |  | V Blank/Through |  |  |  |  |  | 
 |  | Safe Title |  |  |  |  |  | 
 |  | 4:3 Crop |  |  |  |  |  | 
 | AUX Bus | AUX MIX | CH1-12 | CH13-24 |  |  |  | 
 |  | AUX CCR |  |  |  |  |  | 
Multi Viewer | Multi Viewer | Multi Viewer |  |  | CH1 | CH1 | CH2 | CH2
 |  | Board_Name: | XPT-34A (for MVS-3000) |  |  |  |  | 
 |  | SLOT_No: | SLOT5 |  |  |  |  | 
 |  | IC_Name: | OUT | OUT | MV | DDR2 | MV | DDR2
 |  | REF_No: | IC003 | ----- | IC005 | IC1701 | IC006 | IC1703
Output Process | Output | Video Clip | CH1-12 | ----- |  |  |  | 
 |  | V Blank/Through |  |  |  |  |  | 
 |  | Safe Title |  |  |  |  |  | 
 |  | 4:3 Crop |  |  |  |  |  | 
 | AUX Bus | AUX MIX | CH1-12 | ----- |  |  |  | 
 |  | AUX CCR |  |  |  |  |  | 
Multi Viewer | Multi Viewer | Multi Viewer |  |  | CH1 | CH1 | CH2 | CH2

## Slide 13
How to specify the faulty board and a component: DVP-55
 |  | Board_Name: | DVP-55 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | SLOT_No: | MKS-6570：SLOT3 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | IC_Name: | PVFLT | AINTP | CADEC | DDR2 | DDR2 | DDR2 | DDR2 | DDR2 | DDR2 | ZBT-SRAM | DDR2+SRAM | DDR2+SRAM | DDR2+SRAM | DDR2+SRAM | DDR2
 |  | REF_No: | IC2 | IC3 | IC1 | IC1402 | IC1404 | IC1502 | IC1503 | IC2102 | IC2103 | IC2202 | IC1601 | IC1702 | IC1801 | IC1901 | IC2002
Edge | Border/Crop | Border | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Crop | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Beveld Edge | Beveld Edge | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Color Mix | Color Mix | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Video Mod | Defocus/Blur | Defocus | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Blur | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Multi Move | Multi Move |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Color Mod | Color Mod | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Mosaic | Mosaic | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Freeze | Freeze | Hard Freeze | CH1/2 |  |  |  |  |  | CH1/2 |  |  |  |  |  |  |  | 
 |  | Time Strobe | CH1/2 |  |  |  |  |  | CH1/2 |  |  |  |  |  |  |  | 
 |  | Film | CH1/2 |  |  |  |  |  | CH1/2 |  |  |  |  |  |  |  | 
Light/Trail | Ligthing | Ligthing |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Trail | Trail | CH1/2 |  |  |  |  |  |  | CH1/2 | CH1/2 |  |  |  |  |  | 
 | MotionDecay | MotionDecay | CH1/2 |  |  |  |  |  |  | CH1/2 | CH1/2 |  |  |  |  |  | 
 | KF Strobe | KF Strobe | CH1/2 |  |  |  |  |  |  | CH1/2 | CH1/2 |  |  |  |  |  | 
In/Out |  | BKGD | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Process | V Fld/Frm | CH1/2 |  |  |  |  | CH1/2 |  |  |  |  |  |  |  |  | 
 |  | K Fld/Frm | CH1/2 |  |  |  |  | CH1/2 |  |  |  |  |  |  |  |  | 
 |  | Intrpo |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Filter Mode | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Anti Moire Filter | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Graphic | Graphic | CH1/2 |  |  |  |  |  |  |  |  | CH1/2 |  |  |  |  | 
Enhanced Video | Sketch | Sketch | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Modify | Metal | Metal | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Glow | Glow | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Combine | Combine | Combine | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Brick | Brick | Brick | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Shadow | Shadow | Shadow | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Source/Target | Lock Size | Lock Size |  | CH1/2 |  |  |  |  |  |  |  |  | CH1/2 | CH1/2 | CH1/2 | CH1/2 | 
 | Lock XYZ | Lock XYZ |  | CH1/2 |  |  |  |  |  |  |  |  | CH1/2 | CH1/2 | CH1/2 | CH1/2 | 
 | Rot (Spin Mode) | Rot (Spin Mode) |  | CH1/2 |  |  |  |  |  |  |  |  | CH1/2 | CH1/2 | CH1/2 | CH1/2 | 
 | Aspect | Aspect |  | CH1/2 |  |  |  |  |  |  |  |  | CH1/2 | CH1/2 | CH1/2 | CH1/2 | 
Non-Linear | Wave | Wave |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Mosaic Glass | Mosaic Glass |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Flag | Flag |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Twist | Twist |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Ripple | Ripple |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Rings | Rings |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | BrOKen Glass | BrOKen Glass |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Flying Bars | Flying Bars |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Blind | Blind |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Split | Split |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Split Slide | Split Slide |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Mirror | Mirror |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Multi Mirror | Multi Mirror |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Kaleido Scope | Kaleido Scope |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Lens | Lens |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Circle | Circle |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Panorama | Panorama |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Page Turn | Page Turn |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Roll | Roll |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Cylinder | Cylinder |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Sphere | Sphere |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Explosion | Explosion |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Swirl | Swirl |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Melt | Melt |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2
 | Character Trail | Character Trail |  | CH1/2 |  |  |  |  |  |  |  |  |  |  |  |  | CH1/2

## Slide 14
How to specify the faulty board and a component: FC-114

## Slide 15
How to specify the faulty board and a component : FC-114
 |  |  | Board_Name: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | SLOT_No: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | IC_Name: | VENUS | VENUS | VENUS | VENUS | VENUS | VENUS | VENUS | VENUS | DDR | DDR | DDR | DDR | DDR | DDR | DDR | DDR
 |  |  | REF_No: | IC11 | IC12 | IC13 | IC14 | IC15 | IC16 | IC17 | IC18 | IC1501 IC1502 | IC1701 IC1702 | IC1901 IC1902 | IC2101 IC2102 | IC2301 IC2302 | IC2501 IC2502 | IC2701 IC2702 | IC2901 IC2902
Input 1-4 Format | Up Converter | Aspect | Edge Crop | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
5-8 Format |  |  | Squeeze | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Letter Box | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  | Conversion | Frame | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Field | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Adaptive | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  | Edge Crop Position | Position | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Center | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  | Letter Box Position | Position | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Center | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  | Enhancer | Source No. | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Detail Gain | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Limitter | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Crisp | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Level Depend | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Frequency | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | H/V Ratio | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 | Down Converter | Aspect | Edge Crop | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Squeeze | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Letter Box | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  | Edge Crop Position | Position | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Center | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  | Letter Box Position | Position | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Center | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  | Enhancer | Source No. | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Detail Gain | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Limitter | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Crisp | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Level Depend | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | Frequency | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 |  |  | H/V Ratio | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 | Cross Converter |  |  | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8 | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
 | Frame Delay |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Output 1-2 Format | Up Converter | Aspect | Edge Crop |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Squeeze |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Letter Box |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  | Conversion | Frame |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Field |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Adaptive |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  | Edge Crop Position | Position |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Center |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  | Letter Box Position | Position |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Center |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  | Enhancer | Source No. |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Detail Gain |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Limitter |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Crisp |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Level Depend |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Frequency |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | H/V Ratio |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 | Down Converter | Aspect | Edge Crop |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Squeeze |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Letter Box |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  | Edge Crop Position | Position |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Center |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  | Letter Box Position | Position |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Center |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  | Enhancer | Source No. |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Detail Gain |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Limitter |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Crisp |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Level Depend |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | Frequency |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 |  |  | H/V Ratio |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 
 | Cross Converter |  |  |  |  |  |  | CH1 | CH2 |  |  |  |  |  |  | CH1 | CH2 |  | 

## Slide 16
How to specify the faulty board and a component : FC-114
 |  |  | Board_Name: |  |  |  |  |  |  |  | 
 |  |  | SLOT_No: |  |  |  |  |  |  |  | 
 |  |  | IC_Name: | DDR2 | DDR2 | DDR2 | DDR2 | DDR2 | DDR2 | DDR2 | DDR2
 |  |  | REF_No: | IC3101 | IC3103 | IC3201 | IC3203 | IC3301 | IC3303 | IC3401 | IC3403
Input 1-4 Format | Up Converter | Aspect | Edge Crop |  |  |  |  |  |  |  | 
5-8 Format |  |  | Squeeze |  |  |  |  |  |  |  | 
 |  |  | Letter Box |  |  |  |  |  |  |  | 
 |  | Conversion | Frame |  |  |  |  |  |  |  | 
 |  |  | Field |  |  |  |  |  |  |  | 
 |  |  | Adaptive |  |  |  |  |  |  |  | 
 |  | Edge Crop Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Letter Box Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Enhancer | Source No. |  |  |  |  |  |  |  | 
 |  |  | Detail Gain |  |  |  |  |  |  |  | 
 |  |  | Limitter |  |  |  |  |  |  |  | 
 |  |  | Crisp |  |  |  |  |  |  |  | 
 |  |  | Level Depend |  |  |  |  |  |  |  | 
 |  |  | Frequency |  |  |  |  |  |  |  | 
 |  |  | H/V Ratio |  |  |  |  |  |  |  | 
 | Down Converter | Aspect | Edge Crop |  |  |  |  |  |  |  | 
 |  |  | Squeeze |  |  |  |  |  |  |  | 
 |  |  | Letter Box |  |  |  |  |  |  |  | 
 |  | Edge Crop Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Letter Box Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Enhancer | Source No. |  |  |  |  |  |  |  | 
 |  |  | Detail Gain |  |  |  |  |  |  |  | 
 |  |  | Limitter |  |  |  |  |  |  |  | 
 |  |  | Crisp |  |  |  |  |  |  |  | 
 |  |  | Level Depend |  |  |  |  |  |  |  | 
 |  |  | Frequency |  |  |  |  |  |  |  | 
 |  |  | H/V Ratio |  |  |  |  |  |  |  | 
 | Cross Converter |  |  |  |  |  |  |  |  |  | 
 | Frame Delay |  |  | CH1 | CH2 | CH3 | CH4 | CH5 | CH6 | CH7 | CH8
Output 1-2 Format | Up Converter | Aspect | Edge Crop |  |  |  |  |  |  |  | 
 |  |  | Squeeze |  |  |  |  |  |  |  | 
 |  |  | Letter Box |  |  |  |  |  |  |  | 
 |  | Conversion | Frame |  |  |  |  |  |  |  | 
 |  |  | Field |  |  |  |  |  |  |  | 
 |  |  | Adaptive |  |  |  |  |  |  |  | 
 |  | Edge Crop Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Letter Box Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Enhancer | Source No. |  |  |  |  |  |  |  | 
 |  |  | Detail Gain |  |  |  |  |  |  |  | 
 |  |  | Limitter |  |  |  |  |  |  |  | 
 |  |  | Crisp |  |  |  |  |  |  |  | 
 |  |  | Level Depend |  |  |  |  |  |  |  | 
 |  |  | Frequency |  |  |  |  |  |  |  | 
 |  |  | H/V Ratio |  |  |  |  |  |  |  | 
 | Down Converter | Aspect | Edge Crop |  |  |  |  |  |  |  | 
 |  |  | Squeeze |  |  |  |  |  |  |  | 
 |  |  | Letter Box |  |  |  |  |  |  |  | 
 |  | Edge Crop Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Letter Box Position | Position |  |  |  |  |  |  |  | 
 |  |  | Center |  |  |  |  |  |  |  | 
 |  | Enhancer | Source No. |  |  |  |  |  |  |  | 
 |  |  | Detail Gain |  |  |  |  |  |  |  | 
 |  |  | Limitter |  |  |  |  |  |  |  | 
 |  |  | Crisp |  |  |  |  |  |  |  | 
 |  |  | Level Depend |  |  |  |  |  |  |  | 
 |  |  | Frequency |  |  |  |  |  |  |  | 
 |  |  | H/V Ratio |  |  |  |  |  |  |  | 
 | Cross Converter |  |  |  |  |  |  |  |  |  | 

## Slide 17
How to specify the faulty board and a component : MY-119

## Slide 18
2012.11 PSG CCS Dept.1
MVS-6530/6520/3000 Demo Unit
Version Up procedure

## Slide 19: 0. Introduction
  In order to upgrade MVS-6530/MVS-6520/MVS-3000 to V1.00, CPLD and SIO data need to be upgraded together with Application and PFGA upgrade.
  SWR_CPLD(without Xilinx Tool)
    XPT-34/34A Board
    MY-119/119A Board
    DVP-55 Board
  SWR_CPLD (with Xilinx Tool)
    CA-85 : SWR_CADEC
  SIO (with Altera Tool)
    CA-85 : SIO_SWR
    CA-85 : SIO_SCU

## Slide 20: Table of contents
0. Introduction
1. Preparations
2. Version Up Procedure

## Slide 21: 1. Preparations
[Version up data (from ICP panel)]
  Please download all the files from the following FTP site.
    ftp://vspgw.vsp.cpg.sony.co.jp/MVS6500/V100_Demo/
    V100_Demo/Application/
    V100_Demo/SWR_CPLD/
    V100_Demo/SWR_FPGA/
    Copy to USB Memory.
[Version up data (from PC)]
  Please download all the files from the following FTP site.
    ftp://vspgw.vsp.cpg.sony.co.jp/MVS6500/V100_Demo/
    MVS6500_V100_add/
    Copy to PC (C:\MVS6500_V100_add)

## Slide 22: 1. Preparations
[Programming Tool (Xilinx)]
  Programming Tool (Xilinx iMPACT) http://www.xilinx.com/support/download/index.htm - Lab Tools
  * Obtain Lab Tools from the Xilinx download site.
[Programming Tool (Altera)]
  Programming Tool (Altera QuartusII Web Edition & Programming Software) https://www.altera.com/download/dnl-index.jsp
  * Obtain Lab Tools from the Altera download site.
[Required Equipment]
  Windows PC (with a USB port)

## Slide 23: 1. Preparations
[Required Parts]
  Xilinx USB cable (Platform Cable USB II) http://www.xilinx.com/products/boards-and-kits/HW-USB-II-G.htm
  * Purchase it from Xilinx.
  Altera USB cable (USB Blaster Download Cable)
    http://www.altera.com/buy/cables/buy-cables.html
    * Purchase it from Altera.
  ISP connector (SONY Part Number: A-1733-365-A)
  Terminal Cable (RS-232C Cable: SONY Part Number: 1-964-480-11)
Xilinx
Altera
ISP connector(SONY)

## Slide 24: 2. Version Up Procedure
・Installation order
2-1. SWR_CPLD (XPT/MY/DVP board)
2-2. Application Software
2-3. SWR_FPGA
2-4. SWR_CPLD (CA-85)
2-5. SIO (CA-85)

## Slide 25: 2-1. SWR_CPLD (XPT/MY/DVP board)
2-1. SWR_CPLD (XPT/MY/DVP board)
Caution
"SWR_CPLD" must be installed before installing "Proc Application".
If CPLD was not installed first, Proc application can't be installed.
[Upgrade “SWR_CPLD”]
* CPLD can be upgraded by Menu.
* Necessary data is stored in V100_Demo/SWR_CPLD folder.
2-1-1. Go to Installation Menu.
2-1-2. Select the following file name in the Menu.
for MVS-6500: MVS6500-CPLD [V1.00] (for upgrade install)
for MVS-3000: MVS3000-CPLD [V1.00] (for upgrade install)
2-1-3. Execute "Install".
2-1-4. After the installation is completed, turn off and on the processor.

## Slide 26: 2-1. SWR_CPLD (XPT/MY/DVP board)
[How to check the CPLD version]
* CPLD version is not shown in the Menu. In order to check the version, please connect PC terminal.
(a) After booted up, connect the terminal cable to CN702 on the CA-85 board (Baud Rate: 115200 kbps)
(b) XPT-34/34A CADEC
Enter d 0x98020000
Check if 0100 001e is shown at the top of character string.
* If this is not installed correctly, Proc application can't be installed.
(c) DVP-55 CADEC (for MVS-6500 only)
Enter d 0x9b000000
Check if 0100 000e is shown at the top of character string.
* If this is not installed correctly, CCR may not work correctly.
(d) MY-119/119A CADEC
Move the terminal cable to CN603 on the MY-119/119A board
Enter d 0x98020000
Check if 0100 0002 is shown at the top of character string.
* If this is not installed correctly, picture noise may be seen when a parameter is changed for Non-linear effect.

## Slide 27: 2-2. Application Software
2-2. Application Software
[Upgrade “UI, PNL, SWR”]
* Application software can be upgraded by Menu.
* Necessary data is stored in V100_Demo/Application folder.
2-2-1. Go to Installation Menu.
2-2-2. Select the following file name in the Menu.
UI : ICP-6500/3000 UI (Full)
PNL for MVS-6500 : SCU6500 CTRL. “Full” (MAIN BOOT2&APL)
PNL for MVS-3000 : SCU3000 CTRL. “Full” (MAIN BOOT2&APL)
SWR for MVS-6500 : MVS6500 Proc. [V1.00] (for full install)
SWR for MVS-3000 : MVS3000 Proc. [V1.00] (for full install)
2-2-3. Execute "Install".
2-2-4. After the installation is completed, turn off and on the processor.

## Slide 28: 2-3. SWR_FPGA
2-3. SWR_FPGA
[Upgrade “SWR_FPGA”]
* Application software can be upgraded by Menu.
* Necessary data is stored in V100_Demo/SWR_FPGA folder.
2-3-1. Go to Installation Menu.
2-3-2. Select the following file name in the Menu.
SWR for MVS-6500 : MVS6500-FPGA [V1.00] (for full install)
SWR for MVS-3000 : MVS3000-FPGA [V1.00] (for full install)
2-3-3. Execute "Install".
2-3-4. After the installation is completed, turn off and on the processor.

## Slide 29: 2-4. SWR_CPLD (CA-85)
2-4. SWR_CPLD (CA-85)
[Connecting the Xilinx USB cable (Platform Cable USB II) to the ISP connector (SONY Part Number: A-1733-365-A)]
The procedure for connecting Xilinx Platform Cable USB II to the ISP connector is described below.
1. Install the supplied Flying Wires and the Adapter on Platform Cable USB II. [Fig.2-4-1]
2. Connect Flying Wires to the ISP connector as follows. [Fig.2-4-2] Flying Wires ISP connector TCK/CCLK/SCK ------ 1pin – TCK GND/GND/GND ------ 2pin – GND TDO/DONE/MISC----- 3pin – TDO VCC/VCC/VCC ------ 4pin – VCC TMS/PROG/SS ------ 5pin – TMS 6pin – No Connection 7pin – No Connection 8pin – No connection TDI/DIN/MOSI ------ 9pin – TDI 10pin – No Connection HALT/INIT/WP – No Connection

## Slide 30: 2-4. SWR_CPLD (CA-85)
  [Fig. 2-4-1] [Fig. 2-4-2]

## Slide 31: 2-4. SWR_CPLD (CA-85)
Rewriting the CPLD data (using iMPACT GUI)
  2-4-1. Download the “MVS6500_V100_add” folder from the specified software download site and put it directly under C:/.
  2-4-2. Connect the USB cable to the PC. (The driver is automatically installed.)
  2-4-3. When the USB cable becomes usable, the status indicator of Platform Cable USB II lights in orange. [Fig.2-4-3]
[Fig.2-4-3]

## Slide 32: 2-4. SWR_CPLD (CA-85)
  2-4-4. Insert the end of the ISP connector into the EPR2connector on the following printed boards:
      For the CA-85 board (SWR_CPLD): CN4401(EPR2 SWR)
  2-4-5. Turn on the power of MVS Processor. When they are correctly connected, the status indicator of Platform Cable USB II lights in green. [Fig.2-4-5]
[Fig.2-4-4]
[Fig.2-4-5]

## Slide 33: 2-4. SWR_CPLD (CA-85)
    2-4-6. Start Xilinx iMPACT. Start – Program – Xilinx Lab Tools 1x_x – Lab Tool – iMPACT
    2-4-7.When the "Welcome to iMPACT" screen [Fig. 2-4-7] appears during startup, click "Cancel".
    [Fig.2-4-7]

## Slide 34: 2-4. SWR_CPLD (CA-85)
    2-4-8. When the “Automatic Project File Load" screen [Fig. 2-4-8] appears during startup, click “No".
    [Fig.2-4-8]
    2-4-9. When the “Automatically create and save a Project” screen [Fig. 2-4-9] appears during startup, click “No".
    [Fig.2-4-9]

## Slide 35: 2-4. SWR_CPLD (CA-85)
    2-4-10. When the “New iMPACT Project" screen [Fig. 2-4-10] appears during startup, click “Browse".
    [Fig.2-4-10]

## Slide 36: 2-4. SWR_CPLD (CA-85)
    2-4-11. When the “Open iMPACT Project File" screen [Fig. 2-4-10] appears during startup, select
    “C:\MVS6500_V100_add\swr_ca85-12_swr_v1.00_1913\ca85_swr_cpld.ipf".
    [Fig.2-4-11]

## Slide 37: 2-4. SWR_CPLD (CA-85)
    2-4-11. When the “Open iMPACT Project File" screen [Fig. 2-4-11] appears during startup, select
    “C:\MVS6500_V100_add\swr_ca85-12_swr_v1.00_1913\ca85_swr_cpld.ipf".
    [Fig.2-4-11]

## Slide 38: 2-4. SWR_CPLD (CA-85)
    2-4-12. When the following figure [Fig.2-4-12], select “OK”.
    [Fig.2-4-12]

## Slide 39: Rewriting the CPLD data
    If When the “New iMPACT Project" screen [Fig. 2-4-10] does not appear, select Open Project from the File menu. [Fig.2-4-13]
    [Fig.2-4-13]

## Slide 40: 2-4. SWR_CPLD (CA-85)
    2-4-14. The JTAG Chain file is displayed. [Fig. 2-4-14]
    click the first xc3s200an.
    [Fig.2-4-14]

## Slide 41: 2-4. SWR_CPLD (CA-85)
    2-4-15. Write the data to CPLD. Select Program Flash and Load FPGA from the Operations menu to start writing to the device. [Fig. 2-4-15-1] and [Fig. 2-4-15-2] Never turn off the power.
    [Fig.2-4-15-1] [Fig.2-4-15-2]

## Slide 42: 2-4. SWR_CPLD (CA-85)
    2-4-16. Completion of writing When writing is completed with success, "Program Succeeded" is displayed. [Fig.2-4-16]
    After the installation is completed, turn off and on the processor.
    [Fig.2-4-16]

## Slide 43: 2-4. SWR_CPLD (CA-85)
[How to check the CPLD version]
* CPLD version is not shown in the Menu. In order to check the version, please connect PC terminal.
(a) After booted up, connect the terminal cable to CN702 on the CA-85 board (Baud Rate: 115200 kbps)
(b) CA-85 SWR_CADEC
Enter d 0x90100000
Check if 0100 1913 is shown
at the top of character string.
* If this is not installed
correctly, Proc can't be
operated correctly.

## Slide 44: 2-5. SIO (CA-85)
2-5. SIO (CA-85)
[Connecting the Altera USB cable (USB Blaster Download Cable) to the ISP connector (SONY Part Number: A-1733-365-A)]
The procedure for connecting Altera USB Blaster Download Cable to the ISP connector is described below.
1pin
1pin

## Slide 45: 2-5. SIO (CA-85)
Rewriting the SIO data (using QuartusII Programmer GUI)
  2-5-1. Download the “MVS6500_V100_add” folder from the specified software download site and put it directly under C:/.
  2-5-2. Connect the USB cable to the PC. (The driver is automatically installed.)

## Slide 46: 2-5. SWR_CPLD (CA-85)
  At first, the SIO data should be written in SWR.
  2-5-4. Insert the end of the ISP connector into the EPR2connector on the following printed boards:
      For the CA-85 board (SIO_SWR): CN4401(EPR2 SWR)
  2-5-5. Turn on the power of MVS Processor.
[Fig.2-5-4]

## Slide 47: 2-5. SWR_CPLD (CA-85)
    2-5-6. Start Altera QuartusII. Start – Program – Altera 1x_x – QuartusII
    2-5-7. Start Programmer
    Select “Tools – Programmer”. [Fig.2-5-7]
[Fig.2-5-7]

## Slide 48: 2-5. SWR_CPLD (CA-85)
    2-5-8. Select “Auto Detect”.
[Fig.2-5-8]

## Slide 49: 2-5. SWR_CPLD (CA-85)
    2-5-9. When the “Select Device " screen [Fig. 2-5-9] appears, select “EP3C25” and click “Close” button.
[Fig.2-5-9]

## Slide 50: 2-5. SWR_CPLD (CA-85)
    2-5-10. The JTAG Chain file is displayed. [Fig. 2-5-10]
    Duble click “File”(Left side at EP3C25) low.
[Fig.2-5-10]

## Slide 51: 2-5. SWR_CPLD (CA-85)
    2-5-11. When the “Select New Programming File" screen [Fig. 2-5-11] appears, select
    “C:\MVS6500_V100_add\V100_SIO_SWR_wr_file_scu_0915_release\SCU_NIOS.sof".
[Fig.2-5-11]

## Slide 52: 2-5. SWR_CPLD (CA-85)
    2-5-12. Check “Program/Cofigure”.
    Next, select “Start” button.
[Fig.2-5-12]

## Slide 53: 2-5. SWR_CPLD (CA-85)
[Fig.2-5-13]
    2-5-13. SOF File writing is completed.
    Do not remove the cable. NIOS should be written next.

## Slide 54: 2-5. SWR_CPLD (CA-85)
[Fig.2-5-14]
    2-5-14. Start NIOSII xx.x Command Shell. Start – Program – Altera 1x_x – NIOS II EDS xx.x – Start NIOSII xx.x Command Shell

## Slide 55: 2-5. SWR_CPLD (CA-85)
[Fig.2-5-15]
    2-5-15.
    Please enter
    cd c:/MVS6500_V100_add/V100_SIO_SWR_wr_file_scu_0915_release

## Slide 56: 2-5. SWR_CPLD (CA-85)
  2-5-16.
  Please enter
  nios2-flash-programmer --cable="Usb-blaster [USB-0]" --instance=1 --epcs --base=0x02000000 nios_scu.flash
[Fig.2-5-16]

## Slide 57: 2-5. SWR_CPLD (CA-85)
  2-5-17.
  Please enter
  nios2-flash-programmer --cable="Usb-blaster [USB-0]" --instance=1 --epcs --base=0x02000000 nios2sioApl.flash
[Fig.2-5-17]

## Slide 58: 2-5. SWR_CPLD (CA-85)
  2-5-18.
  Please enter
  nios2-flash-programmer --cable="Usb-blaster [USB-0]" --instance=1 --epcs --base=0x02000000 nios2SbusApl.flash
[Fig.2-5-18]

## Slide 59: 2-5. SWR_CPLD (CA-85)
  Next, write the SIO data in SCU.
  2-5-19. Insert the end of the ISP connector into the EPR2connector on the following printed boards:
      For the CA-85 board (SIO_SCU): CN4402(EPR2 SCU)
[Fig.2-5-19]

## Slide 60: 2-5. SWR_CPLD (CA-85)
The following steps are basically the same as SWR SIO write, although the files and commands to be used are different.
  Please use the following files and commands.
  2-5-11.
  C:\MVS6500_V100_add\ V100_SIO_SCU_wr_file_scu_0920_release \SCU_NIOS.sof
  2-5-15.
  cd c:/MVS6500_V100_add/V100_SIO_SWR_wr_file_scu_0920_release
  When finish writing, please turn the power off and then turn it on.

## Slide 61: 2-5. SWR_CPLD (CA-85)
How to verify
Turn the power on of the processor.
After booted, check if the LEDs in the red circle in below picture are blinking on the CA-85 board.
One LED is blinking
Three LEDs are blinking