## Slide 1: Tally Setup while in Resource Share Mode

## Slide 2: Panel 1 System Config
On Panel 1
  1st Sw’er should be SWR1
  2nd Sw’er should be SWR2
  Tally Master should be Enabled

## Slide 3: Panel 2 System Config
On Panel 2
  1st Sw’er should be SWR2
  2nd Sw’er should be SWR1
  Tally Master should be OFF

## Slide 4: Panel 1 Button Tally
On Panel 1
  Set Tally Type to be R1

## Slide 5: Panel 2 Button Tally
On Panel 2
  Set Tally Type to be R2

## Slide 6: Panel 1 Router Address setting
On Panel 1
  SWR1 should be at
    Source = 1
    Destination = 1
    Level = 1
    Matrix Size = 320x348
  SWR2 should be at
    Source = 401
    Destination = 401
    Level = 1
    Matrix Size = 320x348
There is no setting for Alias Name Gp No

## Slide 7: Panel 2 Router Address setting
On Panel 2 (same as Panel 1)
  SWR1 should be at
    Source = 1
    Destination = 1
    Level = 1
    Matrix Size = 320x348
  SWR2 should be at
    Source = 401
    Destination = 401
    Level = 1
    Matrix Size = 320x348
There is no setting for Alias Name Gp No

## Slide 8: SWR1 Program Output confirmation
On Panel 1
  Confirm the LOGICAL Out# for P/P PGM1
    In this case, Logical is 1 and Physical is 1
This information is required to set the Tally Enable

## Slide 9: SWR2 Program Output confirmation
On Panel 2 (same as Panel 1)
  Confirm the LOGICAL Out# for P/P PGM1
    In this case, Logical is 1 and Physical is 13
This information is required to set the Tally Enable

## Slide 10: Panel 1 Tally Enable settings
On Panel 1
  For SWR1, create a R1 Tally Enable for Destination OUT001
    Based on P/P PGM1 logical assignment in menu 7333
  For SWR2, create a R2 Tally Enable for Destination OUT401
    Based on P/P PGM1 logical assignment in menu 7333 on Panel 2

## Slide 11: Panel 2 Tally Enable setting
On Panel 2 (same as Panel 1)
  For SWR1, create a R1 Tally Enable for Destination OUT001
    Based on P/P PGM1 logical assignment in menu 7333 on Panel 1
  For SWR2, create a R2 Tally Enable for Destination OUT401
    Based on P/P PGM1 logical assignment in menu 7333